## Slide 1: Vertical Position Reconstruction Update
Analysis Meeting 7 March 2024
Sam Pratt

## Slide 2: Overview
Work done previously on deceleration effect
New deceleration results from using Bismuth Sources
Next steps
Work done previously on timestamp correction effects
New timestamp results from using Bismuth Sources
Next steps

## Slide 3: Overview of Current Reconstruction
Cell View
Cathode end cap
Cathode end cap
Anode wire

## Slide 4: Overview of Tracker Cell
e-
Anode
Time
Cathode 1
Cathode 2
Measured Signals
Recorded Information
Cell View
T0 - Anode
T1,T2 - Anode
Ttop Cathode
T3,T4 –Anode
Tbot – Cathode
Time

## Slide 5: Reconstruction Procedure
H
h

## Slide 6: Reconstruction Procedure
H
h
Height Calculation

## Slide 7: Reconstruction Procedure
H
h
Assume plasma moves with constant speed
Height Calculation

## Slide 8: Reconstruction Procedure
H
h
Assume plasma moves with constant speed
Height Calculation
Anode
Cathode 1
Cathode 2
t0
tbot
ttop
Time

## Slide 9: Reconstruction Procedure
H
h
Assume plasma moves with constant speed
Height Calculation
Current height formula
Anode
Cathode 1
Cathode 2
t0
tbot
ttop
Time

## Slide 10: Assumptions made in reconstruction
Constant plasma speed:

## Slide 11: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
Time
Voltage

## Slide 12: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
Angle of track doesn’t affect our ability to reconstruct
Time
Voltage

## Slide 13: Plasma Deceleration Effect

## Slide 14: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed

## Slide 15: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed
Expect plasma to decelerate due to voltage drop over anode

## Slide 16: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed
Expect plasma to decelerate due to voltage drop over anode
NEMO-3 accounted for this effect using a correction term

## Slide 17: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed
Expect plasma to decelerate due to voltage drop over anode
NEMO-3 accounted for this effect using a correction term
Deceleration causes difference between reconstructed height and true height

## Slide 18: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed
Expect plasma to decelerate due to voltage drop over anode
NEMO-3 accounted for this effect using a correction term
Deceleration causes difference between reconstructed height and true height
This difference depends on

## Slide 19: Evidence of Deceleration
Propagation time depends on - 2% effect in prop time at max
Individual Cell
Propagation time (ns)
Propagation time (10ns)

## Slide 20: Evidence of Deceleration
Propagation time depends on - 2% effect in prop time at max
Individual Cell
Expected
Propagation time (ns)
Propagation time (ns)
Propagation time (10ns)

## Slide 21: Evidence of Deceleration
Propagation time depends on - 2% effect in prop time at max
Cathode timestamps deviate from expected constant speed values
** NEMO-3 used model of changing deceleration – this could be left over effect or something else
Individual Cell
Propagation time (ns)
Propagation time (10ns)

## Slide 22: Evidence of Deceleration
Propagation time depends on - 2% effect in prop time at max
Cathode timestamps deviate from expected constant speed values
Both these effects are consistent with deceleration of the plasma over time
** NEMO-3 used model of changing deceleration – this could be left over effect or something else
Individual Cell
Propagation time (10ns)
Propagation time (ns)

## Slide 23: Correction
NEMO-3 correction
Basis of nemo-3 correction:
Assumes deceleration halves during propagation
Benefits of nemo-3 correction:
Unitless correction values
Can be customized for each cell/depending on location of cell
Current formula
Deceleration term

## Slide 24: New Results Using Bi-207 Sources

## Slide 25: Using the Bismuth Sources
Looking for further affects of deceleration and calibrating correction
Bi-207 Sources
Tracker

## Slide 26: Using the Bismuth Sources
Looking for further affects of deceleration and calibrating correction

## Slide 27: Using the Bismuth Sources
Looking for further affects of deceleration and calibrating correction
The Bismuth sources have a known spacing in the tracker (42.5cm)

## Slide 28: Using the Bismuth Sources
Looking for further affects of deceleration and calibrating correction
The Bismuth sources have a known spacing in the tracker (42.5cm)
The effects of plasma deceleration mean the measured positions of the sources will be shifted from their true value

## Slide 29: Using the Bismuth Sources
Looking for further affects of deceleration and calibrating correction
The Bismuth sources have a known spacing in the tracker (42.5cm)
The effects of plasma deceleration mean the measured positions of the sources will be shifted from their true value
Exaggerated effects are shown here

## Slide 30: Using the Bismuth Sources
Looking for further affects of deceleration and calibrating correction
The Bismuth sources have a known spacing in the tracker (42.5cm)
The effects of plasma deceleration mean the measured positions of the sources will be shifted from their true value
Exaggerated effects are shown here
Note the middle and end source positions don’t change

## Slide 31: Using the Bismuth Sources
Looking for further affects of deceleration and calibrating correction
The Bismuth sources have a known spacing in the tracker (42.5cm)
The effects of plasma deceleration mean the measured positions of the sources will be shifted from their true value
Exaggerated effects are shown here
Note the middle and end source positions don’t change
The relative source positions should now follow a predictable trend

## Slide 32: Using the Bismuth Sources
Looking for further affects of deceleration and calibrating correction

## Slide 33: Recovering Edge Sources
Currently we can’t obtain straight angle data from the edge sources due to trigger restrictions
1
2
3
4
5
6
7

## Slide 34: Recovering Edge Sources
Currently we can’t obtain straight angle data from the edge sources due to trigger restrictions
Have used angle information from Tomas’ tracking to recover data from these sources
1
2
3
4
5
6
7

## Slide 35: Recovering Edge Sources
Currently we can’t obtain straight angle data from the edge sources due to trigger restrictions
Have used angle information from Tomas’ tracking to recover data from these sources
Results in higher uncertainty on position measurement
(Angle is calculated using data uncorrected for deceleration but the scale of this effect has
been account for)
1
2
3
4
5
6
7

## Slide 36: Recovering Edge Sources
Currently we can’t obtain straight angle data from the edge sources due to trigger restrictions
Have used angle information from Tomas’ tracking to recover data from these sources
Results in higher uncertainty on position measurement
(Angle is calculated using data uncorrected for deceleration but the scale of this effect has
been account for)
For new runs this restriction will be removed
Once have enough data can reperform analysis using straight angle tracks
1
2
3
4
5
6
7

## Slide 37: Results
Data for an individual cell
Expected Trend

## Slide 38: What is plotted?
Data for an individual cell
1
2
3
4
5
6
7
1
2
3
4
5
6
7
True position of source
Measured position of source
(relative to central source)

## Slide 39: Example plots from different cells

## Slide 40: Metrics for the Cell
H

## Slide 41: Metrics for the Cell
H
How/where/when the plasma stops moving in the cathode ring affects the effective height of the cell

## Slide 42: Metrics for the Cell
H
How/where/when the plasma stops moving in the cathode ring affects the effective height of the cell

## Slide 43: Metrics for the Cell
H
How/where/when the plasma stops moving in the cathode ring affects the effective height of the cell
Our correction is sensitive to this height value

## Slide 44: Effective height
42.5cm
At the time of installation the sources had a spacing of 42.5cm

## Slide 45: Effective height
42.5cm
At the time of installation the sources had a spacing of 42.5cm
The shape of the plot depends on the effective height I select
H’=2.9

## Slide 46: Effective height
42.5cm
At the time of installation the sources had a spacing of 42.5cm
The shape of the plot depends on the effective height I select
I can shift the height value until the difference is minimized
H’=2.9
H’=2.8

## Slide 47: Effective height
42.5cm
At the time of installation the sources had a spacing of 42.5cm
The shape of the plot depends on the effective height I select
I can shift the height value until the difference is minimized
H’=2.9
H’=2.8
H’=2.77

## Slide 48: Effective height
42.5cm
At the time of installation the sources had a spacing of 42.5cm
The shape of the plot depends on the effective height I select
I can shift the height value until the difference is minimized
H’=2.9
H’=2.8
H’=2.77
This height calculation is very dependent on the known source spacing value and upper and lower source position reconstruction (which have the largest uncertainties)

## Slide 49: Calibrating the Correction
We can see the effect has been reduced:
***Note: this plot is a very rough indication of the correction effect, this first analysis is heavily dependent on knowledge of angle so the data must be
Refitted in tracking using the new height reconstruction
K=0
K=0.02
***

## Slide 50: Next steps
Repeat Analysis with 0 angle track data after new data is gathered

## Slide 51: Next steps
Repeat Analysis with 0 angle track data after new data is gathered
Investigate variation of ‘best’ effective height between cells

## Slide 52: Next steps
Repeat Analysis with 0 angle track data after new data is gathered
Investigate variation of ‘best’ effective height between cells
Extract deceleration calibration constant for each cell

## Slide 53: Next steps
Repeat Analysis with 0 angle track data after new data is gathered
Investigate variation of ‘best’ effective height between cells
Extract deceleration calibration constant for each cell
Repeat analysis using data from a bismuth run with sources in new positions?

## Slide 54: Timestamp Shift Effect

## Slide 55: Timestamp shift effect
Side view
True drift radius
Birds eye view
Propagation time -> time for plasma to travel across the entire cell

## Slide 56: Timestamp shift effect
Side view
True drift radius
Birds eye view
Propagation time -> time for plasma to travel across the entire cell
Drift time -> Time for avalanche to travel from ionization point to the anode wire

## Slide 57: Timestamp shift effect
Side view
True drift radius
Birds eye view
Propagation time -> time for plasma to travel across the entire cell
Drift time -> Time for avalanche to travel from ionization point to the anode wire
These two times should be independent to one another

## Slide 58: Timestamp shift effect
Side view
True drift radius
Birds eye view
Propagation time -> time for plasma to travel across the entire cell
Drift time -> Time for avalanche to travel from ionization point to the anode wire
These two times should be independent to one another
Any dependance suggests the timestamps are mismeasured and need correcting
Anode waveform
T0 - Anode
T1,T2 - Anode
T3,T4 –Anode
Voltage amplitude
Time

## Slide 59: Evidence of height dependent TS correction effects
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 60: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 61: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Delay between avalanche reaching anode and plasma propagation
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 62: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Delay between avalanche reaching anode and plasma propagation
This delay depends on drift
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 63: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Delay between avalanche reaching anode and plasma propagation
This delay depends on drift
‘jitter’ in signal or physical effect eg. Acceleration
t1-t0
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!
Anode waveform
Voltage amplitude
Time

## Slide 64: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Delay between avalanche reaching anode and plasma propagation
This delay depends on drift
‘jitter’ in signal or physical effect eg. Acceleration
correct t0 as a metric for when plasma starts to move vertically
t1-t0
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 65: Evidence of height dependent TS correction effects
Linear region
Non-linear region
Noise/lowcount
Flat/low count
Propagation time average
Drift time (ns)

## Slide 66: Evidence of height dependent TS correction effects
Propagation time average
Drift time (ns)

## Slide 67: Evidence of height dependent TS correction effects
Propagation time average
Drift time (ns)

## Slide 68: Evidence of height dependent TS correction effects
Effect could be > cm
Propagation time average
Drift time (ns)

## Slide 69: Evidence of height dependent TS correction effects
Effect could be > cm
Ways to correct:
Shift calo timestamps depending on drift time
Have a calibration constant, C, unique to each cell
Propagation time average
Drift time (ns)

## Slide 70: Evidence of height dependent TS correction effects
Effect could be > cm
Ways to correct:
Shift calo timestamps depending on drift time
Have a calibration constant, C, unique to each cell
Propagation time average
Drift time (ns)

## Slide 71: New Results Using Bi-207 Sources

## Slide 72: Bi-207 Timestamp shift effect
Based on previous results we expect our height measurement to depend on drift time

## Slide 73: Bi-207 Timestamp shift effect
Based on previous results we expect our height measurement to depend on drift time
The measured positions of our sources should shift with drift time

## Slide 74: Bi-207 Timestamp shift effect
Based on previous results we expect our height measurement to depend on drift time
The measured positions of our sources should shift with drift time
Do we see this effect?

## Slide 75: Bi-207 Timestamp shift effect
Based on previous results we expect our height measurement to depend on drift time
The measured positions of our sources should shift with drift time
Do we see this effect?
We would expect the shift to be on a scale of 1cm

## Slide 76: Bi-207 Timestamp shift effect
-1.5
1.5
0
Look at dependance of this peak position on drift time

## Slide 77: Bi-207 Timestamp shift effect
-1.5
1.5
0
Look at dependance of this peak position on drift time
Non-linear region
Non-linear region
We see effect ~ 1cm

## Slide 78: Timestamp correction next steps
Investigate relation between position shift and propagation time rise more

## Slide 79: Timestamp correction next steps
Investigate relation between position shift and propagation time rise more
See if timestamp correction reduces this effect

## Slide 80: Timestamp correction next steps
Investigate relation between position shift and propagation time rise more
See if timestamp correction reduces this effect
Calibrate correction for each cell

## Slide 81: Timestamp correction next steps
Investigate relation between position shift and propagation time rise more
See if timestamp correction reduces this effect
Calibrate correction for each cell
Investigate any overlap between the timestamp shift and deceleration effect

## Slide 82: Summary
Deceleration and timestamp shift effects have been seen in the bismuth source data

## Slide 83: Summary
Deceleration and timestamp shift effects have been seen in the bismuth source data
Using the sources has allowed for more accurate estimation of the scale of these effects

## Slide 84: Summary
Deceleration and timestamp shift effects have been seen in the bismuth source data
Using the sources has allowed for more accurate estimation of the scale of these effects
Other information learned about tracker structure (effective height)

## Slide 85: Summary
Deceleration and timestamp shift effects have been seen in the bismuth source data
Using the sources has allowed for more accurate estimation of the scale of these effects
Other information learned about tracker structure (effective height)
Calibrations for each cell can now be made to correct for these effects

## Slide 86: Extra

## Slide 87: Anode time reconstruction
H
h
Current height formula
Anode
t0
Time
Could also use anode timestamps as replacements
To be discussed later

## Slide 88: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
All these assumptions break down at some scale. Goal is to find scale at which they break and estimate uncertainties as a result.
Methods for correcting these effects have also been suggested.
Angle of track doesn’t affect our ability to reconstruct
(+ others …)
Time
Voltage

## Slide 89: Assumption 3 – Angle of track doesn’t affect reconstruction ability
Drift radius

## Slide 90: Assumption 3 – Angle of track doesn’t affect reconstruction ability
Drift radius
Using proportional height calculation we get the wrong height!
Correct drift time, incorrect propagation time
Multiple ionisations occur

## Slide 91: Evidence of angle effect

## Slide 92: Correct for Angle Effect

## Slide 93: Further Assumption – Effective Height
Where in the cathode ring does the plasma movement stop
Or ’At what position are the cathode time measurements taken’
Answer changes effective height of cell H’ in the equation
If all heights will be shifted to centre of cell
Due to different electric field within cathode rings
H
(nemo-3 made a correction)

## Slide 94: Further Assumption – Nearest Ionisation
Drift radius

## Slide 95: Further Assumption – Nearest Ionisation
Ionisation did not take place at nearest point of crossing e- to anode wire
Drift radius

## Slide 96: Further Assumption – Nearest Ionisation
Drift radius
Measure correct propagation time but incorrect (overestimated) drift time
True drift radius
measured drift radius
can we take this into account?

## Slide 97: Further Assumption – Edge Drift Effect
Looked into by NEMO-3
Hard to study in SuperNEMO due to trigger
Minor effect

## Slide 98: Extra – Deceleration Cause Slide 1
Anode wire
…
…
As a plasma propagates over the anode more and more charge is added
The change in potential over the anode corresponds to the discharging of the connected capacitor
This approximates to a linear change in electric field
Linear deceleration of the plasma results
NEMO-3 prototype data
NEMO-3 studied this effect with a prototype tracker
No such study using laser triggering was done on the SN prototype
Anode voltage
High voltage value
Capacatance
R Resistance (components not shown)
Speed of plasma
Deceleration

## Slide 99: Extra – Deceleration Cause Slide 2
NEMO-3 Cell Design
SuperNEMO Cell Design
Very similar designs – Ask about checking if equation is still valid!

## Slide 100: Extra – Deceleration Cause Slide 3
Scale in NEM0-3:
Scale in SuperNEMO:
C2 =1nF
R = 220k
Dec =
RC2 =220 ms
Tp = 40 us
Tp/RC2 = 2e-4
H = ?
Deceleration
C2 =2.2nF
R = 470k
Dec =
RC2 = 1034 ms
Tp = 60 us
Tp/RC2 = 2e-5
H = 3m
Summary:
Has this not been looked into at all in Manchester when testing the
Cells? – look up some more documentation!
Note: io depends on the gas mixture - so will change
If SN has more ionizations per second due to larger E field maybe discharge s quicker?

## Slide 101: Extra – Deceleration Cause Slide 4
Note this was in the anode times not the cathode times
End goal is to use width of distributions to estimate the uncertainty anyway!

## Slide 102: Extra – Deceleration Evidence Slide 1
Width of gaussian increases – statistical way plasma moves
Skew of gaussian increases - deceleration effect
Graph is not a straight line – deceleration effect
Centre of guassian to edge of skew:
2000 at low time
8000 at high time
6000 ns timestamp change
t6
Height’
T6-t6_linear
H_rec

## Slide 103: Extra – Deceleration Model Slide 1
Model 1
Model 2
Model 1 – Constant deceleration
Model 2 – Deceleration ½’s when one plasma reaches near cathode
(model NEMO-3 used based off discharge argument )
Note: Model 2 predicts no change in propagation time with height
Is the change in propagation time we see a residual effect ?

## Slide 104: Extra – Deceleration Model Slide 2
Model 1
Model 2
Model 1 – Constant deceleration
Model 2 – Deceleration ½’s when one plasma reaches near cathode
Position of maxima shift between models
Propagation time
Model 1
Note: Model 2 predicts no change in propagation time with height
Is the change in propagation time we see a residual effect ?

## Slide 105: How does the Plasma Move?
1 Plasma starts moving on first ionization:
Anode wire
Assumes don’t need high E field around anode wire to start vertical motion
2 Plasma starts moving when anode quenched:
Anode wire
Assumes high E field needed to produce enough UV’s so that plasma/ionizations can move longitudinally without being stopped by ethanol/quenching gas
3 Combination of the two:
The plasma moves longitudinally slowly at the start then reaches the wire and moves at full speed
Slow speed at first as less UV emitted in low E region away from anode
Anode wire
***NEMO-3 favoured this explantion (with a big difference)

## Slide 106: Extra - Correction
NEMO-3 correction
Need to verify we see the same effect as they did
Need to verify way of calculating deceleration value is valid
Benefits of nemo-3 correction:
Unitless correction values
Can be customized for each cell/depending on location of cell
Next steps:
Test how this reconstruction affects tracking/location abilities
Check for evidence of changing acceleration
Current correction
If effect<5mm do we need to correct?
Based off approximation
Difference in ts values between current reconstruction and using NEMO-3 reconstruction
Deceleration term

## Slide 107: Overview of Tracker Cell
e-
Anode
Time
Cathode 1
Cathode 2
Electron passes through cell
Avalanche triggered in cell
Plasma reaches near cathode
Plasma reaches far cathode
Sequence of Events
Measured Signals
Recorded Information
Cell View
T0 - Anode
T1,T2,Ttop - Anode + Cathode
T3,T4,Tbot – Anode + Cathode
Time
Time

## Slide 108: Overview of Tracker Cell
e-
Anode
Time
Cathode 1
Cathode 2
Electron passes through cell
Avalanche triggered in cell
Plasma reaches near cathode
Plasma reaches far cathode
Sequence of Events
Measured Signals
Recorded Information
Cell View
T0 - Anode
T1,T2,Ttop - Anode + Cathode
T3,T4,Tbot – Anode + Cathode
Time
Time
t0
t1
t2
t3
t4
t5
t6

## Slide 109: Sequence of Events of a Tracker Hit
Anode
Time
t0
t1
t2
t3
t4
Fix time scales – alternative plot

## Slide 110: Using the Bismuth Sources
Looking for further affects of deceleration and calibrating correction

## Slide 111: Validating angle technique
Can’t obtain straight angle data for the edge sources
Angle of track
Reconstructed height
1
2
3
4
5
6
7
1
2
3
4
5
6
7
**This will change soon – will reperform analysis with straight track data

## Slide 112
Tan theta
Height shift of central peak
Position of each measured peak shifts with angle
Gradient is equal to horizontal distance from the source to the cell
Can use this information to project all the events onto the source position – reconstruct source position with calibration by cell
We need to know exact distance from source to cell to do this – if project using coordinates in Falaise the sources appear blurred

## Slide 113
The angles we’re initially calculated using coordinates affected by the deceleration – is the technique still valid?

## Slide 116
gradient
Source position
Variation in height estimates from the different sources indicate how
Much the angular correction will be affected by deceleration
- a typical variation of around 1mm
- The gradient for each source will be affected by deceleration differently
- 1mm error cant account for 1cm effect we see in position variation

## Slide 117: Corrected Angle
This method works because the effect of deceleration within a 10cm range shifts
The measured positions of hits by the same amount to within 2mm
Allowing us to project back to find the position of the source
And then see the larger effect of height differences between sources and their expected positions (~1cm)
Chose cells at the first layer
Range angle from 60 deg to -60 deg
Project heights onto source position (y=z-tan(theta)*t)
At most this could artificially shift the position of data by 2mm (errors shown on height plot)
12cm
t
End up with a series of defined peaks
(including the edge sources)