## Slide 1: Vertical Position Reconstruction Update
SuperNEMO Collaboration Meeting 2024 Marseille
Sam Pratt

## Slide 2: Outline
Overview of current vertical position reconstruction procedure in the tracker

## Slide 3: Outline
Overview of current vertical position reconstruction procedure in the tracker
Highlight potential problems with the current method

## Slide 4: Outline
Overview of current vertical position reconstruction procedure in the tracker
Highlight potential problems with the current method
Suggests corrections to the current reconstruction method

## Slide 5: Outline
Overview of current vertical position reconstruction procedure in the tracker
Highlight potential problems with the current method
Suggests corrections to the current reconstruction method
Give overview of uncertainty on vertical position of passing electrons

## Slide 6: Overview of Tracker
Aerial View
Side View
Tracker Cell
x113
x9
Tracker Array
Full Detector
Tracker Array (side view)
Will summarise recorded information from the tracker

## Slide 7: Overview of Current Reconstruction
Cell View
Cathode end cap
Cathode end cap
Anode wire

## Slide 8: Overview of Tracker Cell
e-
Anode signal*
Cathode 1 signal*
Cathode 2 signal*
Measured Signals
Cell View
Time
Time
Time
*Differential of the voltage measured over the component

## Slide 9: Overview of Tracker Cell
e-
Anode
Cathode 1
Cathode 2
Measured Signals
Recorded Information
Cell View
Time
Electron passes through cell

## Slide 10: Overview of Tracker Cell
e-
Anode
Cathode 1
Cathode 2
Measured Signals
Recorded Information
Cell View
T0 - Anode
Time
t0
Avalanche triggered in cell

## Slide 11: Overview of Tracker Cell
e-
Anode
Cathode 1
Cathode 2
Measured Signals
Recorded Information
Cell View
T0 - Anode
T1,T2 - Anode
Ttop Cathode
Time
t0
t1
t3
ttop
Plasma reaches near cathode

## Slide 12: Overview of Tracker Cell
e-
Anode
Time
Cathode 1
Cathode 2
Measured Signals
Recorded Information
Cell View
T0 - Anode
T1,T2 - Anode
Ttop Cathode
T3,T4 –Anode
Tbot – Cathode
Time
t0
t1
t3
t2
t4
ttop
tbot
Plasma reaches far cathode

## Slide 13: Overview of Tracker Cell
e-
Anode
Time
Cathode 1
Cathode 2
Measured Signals
Recorded Information
Cell View
T0 - Anode
T1,T2 - Anode
Ttop Cathode
T3,T4 –Anode
Tbot – Cathode
Time

## Slide 14: Reconstruction Procedure
Time
e-

## Slide 15: Reconstruction Procedure
H
h

## Slide 16: Reconstruction Procedure
H
h
Height Calculation

## Slide 17: Reconstruction Procedure
H
h
Assume plasma moves with constant speed
Height Calculation

## Slide 18: Reconstruction Procedure
H
h
Assume plasma moves with constant speed
Height Calculation
Anode
Cathode 1
Cathode 2
t0
tbot
ttop
Time

## Slide 19: Reconstruction Procedure
H
h
Assume plasma moves with constant speed
Height Calculation
Current height formula
Anode
Cathode 1
Cathode 2
t0
tbot
ttop
Time

## Slide 20: Assumptions made in reconstruction
Constant plasma speed:

## Slide 21: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
Time
Voltage

## Slide 22: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
Angle of track doesn’t affect our ability to reconstruct
Time
Voltage

## Slide 23: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
All these assumptions break down at some scale. Goal is to find scale at which they break and estimate uncertainties as a result.
Methods for correcting these effects have also been suggested.
Angle of track doesn’t affect our ability to reconstruct
(+ others …)
Time
Voltage

## Slide 24: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
All these assumptions break down at some scale. Goal is to find scale at which they break and estimate uncertainties as a result.
Methods for correcting these effects have also been suggested.
Angle of track doesn’t affect our ability to reconstruct
(+ others …)
Time
Voltage

## Slide 25: Assumption 1 – Constant Plasma Speed
Previously assumed plasma moves with constant speed
H
h

## Slide 26: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed
Expect plasma to decelerate due to voltage drop over anode

## Slide 27: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed
Expect plasma to decelerate due to voltage drop over anode
Voltage change is related to discharge of a capacitor connected to anode
Anode wire
…
…

## Slide 28: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed
Expect plasma to decelerate due to voltage drop over anode
Voltage change is related to discharge of a capacitor connected to anode
NEMO-3 accounted for this effect using a correction term
Anode wire
…
…

## Slide 29: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed
Expect plasma to decelerate due to voltage drop over anode
Voltage change is related to discharge of a capacitor connected to anode
NEMO-3 accounted for this effect using a correction term
Deceleration causes difference between reconstructed height and true height

## Slide 30: Assumption 1 – Constant Plasma Speed
H
h
Previously assumed plasma moves with constant speed
Expect plasma to decelerate due to voltage drop over anode
Voltage change is related to discharge of a capacitor connected to anode
NEMO-3 accounted for this effect using a correction term
Deceleration causes difference between reconstructed height and true height
This difference depends on

## Slide 31: Evidence of Deceleration
Propagation time depends on - 2% effect in prop time at max
Individual Cell
Propagation time (ns)
Propagation time (10ns)

## Slide 32: Evidence of Deceleration
Propagation time depends on - 2% effect in prop time at max
Individual Cell
Expected
Propagation time (ns)
Propagation time (ns)
Propagation time (10ns)

## Slide 33: Evidence of Deceleration
Propagation time depends on - 2% effect in prop time at max
Cathode timestamps deviate from expected constant speed values
** NEMO-3 used model of changing deceleration – this could be left over effect or something else
Individual Cell
Propagation time (ns)
Propagation time (10ns)

## Slide 34: Evidence of Deceleration
Propagation time depends on - 2% effect in prop time at max
Cathode timestamps deviate from expected constant speed values
Both these effects are consistent with deceleration of the plasma over time
** NEMO-3 used model of changing deceleration – this could be left over effect or something else
Individual Cell
Propagation time (10ns)
Propagation time (ns)

## Slide 35: Scale of effect
Change in propagation time from centre to edge of cell
Deviation in cathode timestamp over height

## Slide 36: Scale of effect
Change in propagation time from centre to edge of cell
Suggests deceleration scale:
Deviation in cathode timestamp over height

## Slide 37: Scale of effect
Change in propagation time from centre to edge of cell
Suggests deceleration scale:
NEMO-3
Deviation in cathode timestamp over height

## Slide 38: Scale of effect
Change in propagation time from centre to edge of cell
Suggests deceleration scale:
Suggests prop time estimate is an underestimate – we get cancellation effects due to non-constant deceleration
NEMO-3
Deviation in cathode timestamp over height

## Slide 39: Scale of effect
Change in propagation time from centre to edge of cell
Suggests deceleration scale:
NEMO-3 corrected difference was 8mm
Suggests prop time estimate is an underestimate – we get cancellation effects due to non-constant deceleration
Effect could range from 1mm to >1cm
NEMO-3
Deviation in cathode timestamp over height

## Slide 40: Correction
NEMO-3 correction

## Slide 41: Correction
NEMO-3 correction
Current formula
Deceleration term

## Slide 42: Correction
NEMO-3 correction
Basis of nemo-3 correction:
Assumes deceleration halves during propagation
Current formula
Difference in ts values between current reconstruction and using NEMO-3 reconstruction
Deceleration term

## Slide 43: Correction
NEMO-3 correction
Basis of nemo-3 correction:
Assumes deceleration halves during propagation
Benefits of nemo-3 correction:
Unitless correction values
Can be customized for each cell/depending on location of cell
Current formula
Difference in ts values between current reconstruction and using NEMO-3 reconstruction
Deceleration term

## Slide 44: Correction
NEMO-3 correction
Basis of nemo-3 correction:
Assumes deceleration halves during propagation
Benefits of nemo-3 correction:
Unitless correction values
Can be customized for each cell/depending on location of cell
Next steps:
Need to verify we see the same effect as they did
Current formula
Deceleration term

## Slide 45: Correction
NEMO-3 correction
Basis of nemo-3 correction:
Assumes deceleration halves during propagation
Benefits of nemo-3 correction:
Unitless correction values
Can be customized for each cell/depending on location of cell
Next steps:
Need to verify we see the same effect as they did
Need to verify way of calculating deceleration value is valid
Current formula
Deceleration term

## Slide 46: Correction
NEMO-3 correction
Basis of nemo-3 correction:
Assumes deceleration halves during propagation
Benefits of nemo-3 correction:
Unitless correction values
Can be customized for each cell/depending on location of cell
Next steps:
Need to verify we see the same effect as they did
Need to verify way of calculating deceleration value is valid
Test how this reconstruction affects tracking/location abilities
Current formula
Deceleration term

## Slide 47: Correction
NEMO-3 correction
Basis of nemo-3 correction:
Assumes deceleration halves during propagation
Benefits of nemo-3 correction:
Unitless correction values
Can be customized for each cell/depending on location of cell
Next steps:
Need to verify we see the same effect as they did
Need to verify way of calculating deceleration value is valid
Test how this reconstruction affects tracking/location abilities
Current formula
If effect<5mm do we need to correct?
Difference in ts values between current reconstruction and using NEMO-3 reconstruction
Deceleration term

## Slide 48: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
All these assumptions break down at some scale. Goal is to find scale at which they break and estimate uncertainties as a result.
Methods for correcting these effects have also been suggested.
Angle of track doesn’t affect our ability to reconstruct
(+ others …)
Time
Voltage

## Slide 49: Assumption 2 – Timestamps don’t need correcting
Anode waveform
If prop time changes more when using
Anode time measurements would be
Perfect metric for that !
Does t5 to t6 change with height ?

## Slide 50: Assumption 2 – Timestamps don’t need correcting
Anode waveform
If prop time changes more when using
Anode time measurements would be
Perfect metric for that !
Does t5 to t6 change with height ?
Upper threshold
Lower threshold

## Slide 51: Assumption 2 – Timestamps don’t need correcting
Anode waveform
If prop time changes more when using
Anode time measurements would be
Perfect metric for that !
Does t5 to t6 change with height ?
Upper threshold
Lower threshold
Range 1
Range 2
Range 3
T0 indicates when the initial avalanche reaches the anode wire

## Slide 52: Assumption 2 – Timestamps don’t need correcting
Anode waveform
If prop time changes more when using
Anode time measurements would be
Perfect metric for that !
Does t5 to t6 change with height ?
Upper threshold
Lower threshold
Range 1
Range 2
Range 3
T0 indicates when the initial avalanche reaches the anode wire
Previously assumed it also indicates time the plasma starts to move vertically

## Slide 53: Assumption 2 – Timestamps don’t need correcting
Anode waveform
If prop time changes more when using
Anode time measurements would be
Perfect metric for that !
Does t5 to t6 change with height ?
Upper threshold
Lower threshold
Range 1
Range 2
Range 3
T0 indicates when the initial avalanche reaches the anode wire
Previously assumed it also indicates time the plasma starts to move vertically
Is there an offset?

## Slide 54: Assumption 2 – Timestamps don’t need correcting
Anode waveform
If prop time changes more when using
Anode time measurements would be
Perfect metric for that !
Does t5 to t6 change with height ?
Upper threshold
Lower threshold
Range 1
Range 2
Range 3
T0 indicates when the initial avalanche reaches the anode wire
Previously assumed it also indicates time the plasma starts to move vertically
Is there an offset?
At what time in range 1 does the plasma start to move?

## Slide 55: Assumption 2 – Timestamps don’t need correcting
Anode waveform
If prop time changes more when using
Anode time measurements would be
Perfect metric for that !
Does t5 to t6 change with height ?
Upper threshold
Lower threshold
Range 1
Range 2
Range 3
T0 indicates when the initial avalanche reaches the anode wire
Previously assumed it also indicates time the plasma starts to move vertically
Is there an offset?
At what time in range 1 does the plasma start to move?
At what time in ranges 2 and 3 does the plasma stop?

## Slide 56: Scale of Effect from Real Waveform
Range of anode waveform dip ~ 4us
Total effect on propagation time >10% propagation time
Possible effect on height measurements:
>5%

## Slide 57: Evidence of height dependent TS correction effects
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 58: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 59: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Delay between avalanche reaching anode and plasma propagation
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 60: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Delay between avalanche reaching anode and plasma propagation
This delay depends on drift
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 61: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Delay between avalanche reaching anode and plasma propagation
This delay depends on drift
‘jitter’ in signal or physical effect eg. Acceleration
t1-t0
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 62: Evidence of height dependent TS correction effects
Dependance of propagation time on drift time ~ 10% effect
Delay between avalanche reaching anode and plasma propagation
This delay depends on drift
‘jitter’ in signal or physical effect eg. Acceleration
correct t0 as a metric for when plasma starts to move vertically
t1-t0
Drift time (ns)
Propagation time
Propagation time average
Drift time (ns)
Fix/add more events!!!!

## Slide 63: Evidence of height dependent TS correction effects
Linear region
Non-linear region
Noise/lowcount
Flat/low count
Propagation time average
Drift time (ns)

## Slide 64: Evidence of height dependent TS correction effects
Propagation time average
Drift time (ns)

## Slide 65: Evidence of height dependent TS correction effects
Propagation time average
Drift time (ns)

## Slide 66: Evidence of height dependent TS correction effects
Effect could be > cm
Propagation time average
Drift time (ns)

## Slide 67: Evidence of height dependent TS correction effects
Effect could be > cm
Ways to correct:
Shift calo timestamps depending on drift time
Have a calibration constant, C, unique to each cell
Propagation time average
Drift time (ns)

## Slide 68: Evidence of height dependent TS correction effects
Effect could be > cm
Ways to correct:
Shift calo timestamps depending on drift time
Have a calibration constant, C, unique to each cell
Need to verify if effect is due to ts measurement
Test how this reconstruction affects tracking/ location abilities
Next steps:
Propagation time average
Drift time (ns)

## Slide 69: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
All these assumptions break down at some scale. Goal is to find scale at which they break and estimate uncertainties as a result.
Methods for correcting these effects have also been suggested.
Angle of track doesn’t affect our ability to reconstruct
(+ others …)
Time
Voltage

## Slide 70: Vertical Position Uncertainty Overview
Min resolution of time timestamps: 12.5ns

## Slide 71: Vertical Position Uncertainty Overview
Min resolution of time timestamps: 12.5ns
Expect true error of timestamp, , to scale like a count
is the average time between successive avalanches

## Slide 72: Vertical Position Uncertainty Overview
Min resolution of time timestamps: 12.5ns
Expect true error of timestamp, , to scale like a count
is the average time between successive avalanches
Added errors due to previously mentioned effects
Deceleration: 200ns-1000ns
Timestamp shift: +1000ns

## Slide 73: Vertical Position Uncertainty Overview
Min resolution of time timestamps: 12.5ns
Expect true error of timestamp, , to scale like a count
is the average time between successive avalanches
Added errors due to previously mentioned effects
Deceleration: 200ns-1000ns
Timestamp shift: +1000ns
Current study doesn’t show this trend, need to repeat on individual cell level (more stats)

## Slide 74: Vertical Position Uncertainty Overview
Min resolution of time timestamps: 12.5ns
Expect true error of timestamp, , to scale like a count
is the average time between successive avalanches
Added errors due to previously mentioned effects
Deceleration: 200ns-1000ns
Timestamp shift: +1000ns
Current study doesn’t show this trend, need to repeat on individual cell level (more stats)
Similarly we expect this trend for propagation time uncertainty against height

## Slide 75: Summary
Multiple effects which affect the z reconstruction resolution >5% have been seen

## Slide 76: Summary
Multiple effects which affect the z reconstruction resolution >5% have been seen
Estimates of the error and how the error scales with distance/drift time have been shown

## Slide 77: Summary
Multiple effects which affect the z reconstruction resolution >5% have been seen
Estimates of the error and how the error scales with distance/drift time have been shown
Possible corrections for the reconstruction analysis have been suggested

## Slide 78: Summary
Multiple effects which affect the z reconstruction resolution >5% have been seen
Estimates of the error and how the error scales with distance/drift time have been shown
Possible corrections for the reconstruction analysis have been suggested
Next steps: Verify understanding of corrections, see how corrections affect tracking/locating

## Slide 79: Thanks

## Slide 80: Extra Slides

## Slide 81: Anode time reconstruction
H
h
Current height formula
Anode
t0
Time
Could also use anode timestamps as replacements
To be discussed later

## Slide 82: Assumptions made in reconstruction
Constant plasma speed:
Timestamps do not need to be corrected before being used in reconstruction
All these assumptions break down at some scale. Goal is to find scale at which they break and estimate uncertainties as a result.
Methods for correcting these effects have also been suggested.
Angle of track doesn’t affect our ability to reconstruct
(+ others …)
Time
Voltage

## Slide 83: Assumption 3 – Angle of track doesn’t affect reconstruction ability
Drift radius

## Slide 84: Assumption 3 – Angle of track doesn’t affect reconstruction ability
Drift radius
Using proportional height calculation we get the wrong height!
Correct drift time, incorrect propagation time
Multiple ionisations occur

## Slide 85: Evidence of angle effect

## Slide 86: Correct for Angle Effect

## Slide 87: Further Assumption – Effective Height
Where in the cathode ring does the plasma movement stop
Or ’At what position are the cathode time measurements taken’
Answer changes effective height of cell H’ in the equation
If all heights will be shifted to centre of cell
Due to different electric field within cathode rings
H
(nemo-3 made a correction)

## Slide 88: Further Assumption – Nearest Ionisation
Drift radius

## Slide 89: Further Assumption – Nearest Ionisation
Ionisation did not take place at nearest point of crossing e- to anode wire
Drift radius

## Slide 90: Further Assumption – Nearest Ionisation
Drift radius
Measure correct propagation time but incorrect (overestimated) drift time
True drift radius
measured drift radius
can we take this into account?

## Slide 91: Further Assumption – Edge Drift Effect
Looked into by NEMO-3
Hard to study in SuperNEMO due to trigger
Minor effect

## Slide 92: Extra – Deceleration Cause Slide 1
Anode wire
…
…
As a plasma propagates over the anode more and more charge is added
The change in potential over the anode corresponds to the discharging of the connected capacitor
This approximates to a linear change in electric field
Linear deceleration of the plasma results
NEMO-3 prototype data
NEMO-3 studied this effect with a prototype tracker
No such study using laser triggering was done on the SN prototype
Anode voltage
High voltage value
Capacatance
R Resistance (components not shown)
Speed of plasma
Deceleration

## Slide 93: Extra – Deceleration Cause Slide 2
NEMO-3 Cell Design
SuperNEMO Cell Design
Very similar designs – Ask about checking if equation is still valid!

## Slide 94: Extra – Deceleration Cause Slide 3
Scale in NEM0-3:
Scale in SuperNEMO:
C2 =1nF
R = 220k
Dec =
RC2 =220 ms
Tp = 40 us
Tp/RC2 = 2e-4
H = ?
Deceleration
C2 =2.2nF
R = 470k
Dec =
RC2 = 1034 ms
Tp = 60 us
Tp/RC2 = 2e-5
H = 3m
Summary:
Has this not been looked into at all in Manchester when testing the
Cells? – look up some more documentation!
Note: io depends on the gas mixture - so will change
If SN has more ionizations per second due to larger E field maybe discharge s quicker?

## Slide 95: Extra – Deceleration Cause Slide 4
Note this was in the anode times not the cathode times
End goal is to use width of distributions to estimate the uncertainty anyway!

## Slide 96: Extra – Deceleration Evidence Slide 1
Width of gaussian increases – statistical way plasma moves
Skew of gaussian increases - deceleration effect
Graph is not a straight line – deceleration effect
Centre of guassian to edge of skew:
2000 at low time
8000 at high time
6000 ns timestamp change
t6
Height’
T6-t6_linear
H_rec

## Slide 97: Extra – Deceleration Model Slide 1
Model 1
Model 2
Model 1 – Constant deceleration
Model 2 – Deceleration ½’s when one plasma reaches near cathode
(model NEMO-3 used based off discharge argument )
Note: Model 2 predicts no change in propagation time with height
Is the change in propagation time we see a residual effect ?

## Slide 98: Extra – Deceleration Model Slide 2
Model 1
Model 2
Model 1 – Constant deceleration
Model 2 – Deceleration ½’s when one plasma reaches near cathode
Position of maxima shift between models
Propagation time
Model 1
Note: Model 2 predicts no change in propagation time with height
Is the change in propagation time we see a residual effect ?

## Slide 99: How does the Plasma Move?
1 Plasma starts moving on first ionization:
Anode wire
Assumes don’t need high E field around anode wire to start vertical motion
2 Plasma starts moving when anode quenched:
Anode wire
Assumes high E field needed to produce enough UV’s so that plasma/ionizations can move longitudinally without being stopped by ethanol/quenching gas
3 Combination of the two:
The plasma moves longitudinally slowly at the start then reaches the wire and moves at full speed
Slow speed at first as less UV emitted in low E region away from anode
Anode wire
***NEMO-3 favoured this explantion (with a big difference)

## Slide 100: Extra - Correction
NEMO-3 correction
Need to verify we see the same effect as they did
Need to verify way of calculating deceleration value is valid
Benefits of nemo-3 correction:
Unitless correction values
Can be customized for each cell/depending on location of cell
Next steps:
Test how this reconstruction affects tracking/location abilities
Check for evidence of changing acceleration
Current correction
If effect<5mm do we need to correct?
Based off approximation
Difference in ts values between current reconstruction and using NEMO-3 reconstruction
Deceleration term

## Slide 101: Overview of Tracker Cell
e-
Anode
Time
Cathode 1
Cathode 2
Electron passes through cell
Avalanche triggered in cell
Plasma reaches near cathode
Plasma reaches far cathode
Sequence of Events
Measured Signals
Recorded Information
Cell View
T0 - Anode
T1,T2,Ttop - Anode + Cathode
T3,T4,Tbot – Anode + Cathode
Time
Time

## Slide 102: Overview of Tracker Cell
e-
Anode
Time
Cathode 1
Cathode 2
Electron passes through cell
Avalanche triggered in cell
Plasma reaches near cathode
Plasma reaches far cathode
Sequence of Events
Measured Signals
Recorded Information
Cell View
T0 - Anode
T1,T2,Ttop - Anode + Cathode
T3,T4,Tbot – Anode + Cathode
Time
Time
t0
t1
t2
t3
t4
t5
t6

## Slide 103: Sequence of Events of a Tracker Hit
Anode
Time
t0
t1
t2
t3
t4
Fix time scales – alternative plot